## Slide 1: Project Idea
Curcio Salvatore MAT. 263696
Rabbia Marco MAT. 269211
Voci Gregorio MAT. 263711

## Slide 2: Available Device
Aigital N300 Repeater
WiFi repeater that has been available online for several years for a few tens of euros.
It has several vulnerabilities:
  CVE-2023-30404, Remote Code Execution (RCE) with critical severity;
  CVE-2023-30405, Cross-Site Scripting (XSS) with medium severity.

## Slide 3: Main STEPS
As previously observed, the WiFi repeater suffers from two known vulnerabilities: CVE-2023-30404 and CVE-2023-30405. Following the dump of the device’s EEPROM memory and an analysis of our possibilities, we defined the following steps:
Step 1: Exploit the vulnerabilities to create an attack scenario in which we obtain full control of the device in order to attack other devices on the same network;
Step 2: Firmware extraction and analysis;
Step 3: Develop a firmware version in which we attempt to mitigate these vulnerabilities.

## Slide 4: STEP 1
The first step involves exploiting a Remote Code Execution (RCE) vulnerability present in the firmware of the IoT device.
Through this vulnerability, we achieve the execution of arbitrary code on the embedded system and obtain a reverse shell toward an externally controlled machine.
This allows persistent remote access and administrative control over the device.
Subsequently, the compromised device is used as a point to perform a Man-in-the-Middle (MITM) attack through ARP poisoning.
This enables the interception of network traffic in order to identify sensitive data and credentials, while forwarding the packets to their original destination to maintain the transparency of the attack.

## Slide 5: STEP 2
The second step consists of extracting the firmware directly from the device’s non-volatile memory (EEPROM/flash) through a hardware interface (SOIC clip), preserving its contents without physically removing the chip.
The extracted firmware is then analyzed in order to:
identify the internal structure and filesystem;
locate the vulnerable binary components related to both the RCE and XSS vulnerabilities;
understand the execution flows involved in the vulnerability.
This phase provides a complete view of the device’s software and constitutes the foundation for mitigation activities without relying on the original source code.

## Slide 6: STEP 3
The RCE vulnerability is caused by an unused function within the firmware that was not removed by the developer.
The XSS vulnerability, on the other hand, results from the absence of proper input sanitization during the handling of web requests.
To address these issues, the firmware must be patched by performing binary patching of the code.
The firmware update will be carried out through two possible approaches:
flashing the EEPROM memory;
using the device’s web interface for firmware updates.

## Slide 7: Thanks for your kind attention